Instructions for use
ETHILOOP™
SILICONE SLING
– STERILE –
DESCRIPTION
ETHILOOP™ is an elastic tubing made from biocompatible silicone and is available in diameters of 1.3 and 2.0 mm as well as in sheathed form with a diameter of 1.1 mm. ETHILOOP™ comes in the following colours: white (Color Index Number 77891), red (CI Numbers 71137, 71105, 77891), blue (CI Numbers 77343, 77891, 77502) and yellow (CI Number 77788).
INDICATIONS
ETHILOOP™ is used to secure and label arteries, veins and nerves as well as ureters and the vas deferens.
PERFORMANCE
The elasticity of ETHILOOP™ allows it to be tightened in a controlled way without injuring the tissue involved. During tightening, ETHILOOP™ tubing flattens out, the surface area increases, pressure is distributed over a greater area and the risk of slicing into tissue is minimized.
CONTRAINDICATIONS
None known.
WARNINGS/PRECAUTIONS/INTERACTIONS
ETHILOOP™ has been developed for use during surgery and is not intended for implantation. All needles except bicolor needles labelled with MRI are magnetizable and should therefore not be used in an active magnetic field.
STERILITY
ETHILOOP™ silicone sling is a sterile product. Do not resterilize! Do not use if the package is damaged or opened! Discard opened, unused products!
Page: 2
STORAGE
Recommended storage conditions: below 25° C, away from moisture and direct heat. Do not use after expiry date!
SYMBOLS USED ON LABELLING
￼	=	Do not reuse
￼	=	Use by – year and month
￼	=	Sterile unless package is damaged or opened. Method of sterilization: Irradiation
￼	=	CE-mark and Identification number of Notified Body. The product meets the essential requirements of Medical Device Directive 93/42/EEC
￼	=	Batch number
￼	=	See instructions for use